## Slide 1
High Performance Matrix-Free
Method for Large-Scale FEA
on GPUs
Petros Apostolou, Florian Dugast and Albert To*
Dept. of Mechanical Engineering and Materials Science
University of Pittsburgh
April-02-2020

## Slide 2: Outline
Problem Statement
Finite Element System Formulation
Necessity of Matrix-Free Method
State of the Art
CPU Matrix-Free Conjugate Gradient
GPU Matrix-Free Conjugate Gradient
Contribution
Future Research
1-3 Introduction
4-6 Method
7-8 Results

## Slide 3: Problem Statement
Boundary Conditions (Dirichlet):
3D Steady-State Heat Conduction (Isotropic thermal conductivity k) :
0
1

## Slide 4: Finite Element System Formulation
“Weak” form of the heat conduction equation (Galerkin method):
N = [N1 N2 … N8]: shape functions for the
8-node finite element (hexahedron) N1 = 1/8 (1-ξ)(1-n)(1-ζ)
[Ke]{Te} = {Fe}: finite element system for ele. e
Ke[8 x 8] = BTB: where B =
KT = F
K: global conductivity matrix
T: temperature field
F: heat source vector

## Slide 5: Necessity of Matrix-Free Method
K
[N x N]
T
F
[N x 1]
[N x 1]
Size[K] becomes a major bottleneck for large sizes (e.g. N > 10M):
N becomes λN  [λN x λN] = (λΝ)2  Expensive (λ = 1,2,3,...)
Sparse-matrix storage is NOT enough  Exceeds memory limits
Suggestion:
Matrix-free method allows for larger size domains by avoiding the global matrix assembly  [N x N] is not necessary to be stored or computed

## Slide 6: Necessity of Matrix-Free Method
e1
e2
e3
e4
Writing the linear finite equation for node 2:
Assuming:
K
T
F
If local to global
nodal values
transfers are given
then instead of K
only Ke is needed!!
K3
K2
K4
K1

## Slide 7: Necessity of Matrix-Free Method
Voxel-based technique in hexahedral mesh:
N = [nx x ny x nz] : mesh nodes
id = i + (nx x j) + [(nx x ny ) x k]
node(id+1) = node(id) + 1
row(id+1) = row(id) + 1
slice(id+1) = slice(id) + 1
e  id  edof[id]
Regular connectivity facilitates matrix-free methods
nx
nz
ny
N
row
slice
j
i
k

## Slide 8: State of the Art
Matrix-Free Methods:
Thomas Hughes “An element-by-element solution algorithm for problems of structural and solid mechanics”. Division of Applied Mechanics, Durand Building, Stanford University, Stanford, August 1982, U.S.A. [1st Instance]
J.M.Frutos & D.H.Perez “Efficient matrix-free GPU implementation of Fixed Grid Finite Element Analysis” Department of Structures and Construction, Technical University of Cartagena, May 2015 Spain. [20 x Speed-Up – 1 GPU]
Pros: Significant savings in computational time and memory
Cons: Difficult for Unstructured Mesh and Complex Boundaries

## Slide 9: CPU Matrix-Free Conjugate Gradient
T  0 (initial guess)
r  KT – F (residual)
Matrix-Free MV
Compute line search
Compute rnorm
While
[rnorm > ε = 10-6 ]
Update Matrix-Free MV(dst,Ke,src)
Compute Conjugate Direction α
update T = T + a * src
update r = r – a * dst
update rnorm =
Update line search and help vectors
TRUE
Convergence
reference: https://en.wikipedia.org/wiki/Conjugate_gradient_method
rnorm = ε, KT – F = 0

## Slide 10: CPU Matrix-Free Conjugate Gradient
Matrix-Free MV(dst, Ke, src):
set dst  0
for element in mesh
for rows in Ke[8 x 8]
extract rowindex
define tmp  0
for nodes in element
extract DOFindex
tmp = tmp + Ke * src
end
dst = dst + tmp
end
end
! impose Dirichlet BC
for element in mesh
if [element == face]
src  0
dst  0
end
end
return dst
MFMV consumes 80% out of the total computations

## Slide 11: CPU Matrix-Free Conjugate Gradient
Computational Time on CPU:
Memory usage on CPU:
MFCG is 23.84 x times faster than the global matrix assembly solver
MFCG consumes 43.42 x times less memory

## Slide 12: CPU Matrix-Free Conjugate Gradient
Relative numerical error :
Dirichlet BC: T = 0 is satisfied on boundary faces
Verification of the numerical results with the PETSc library
Ref: https://www.mcs.anl.gov/petsc/

## Slide 13: CPU Matrix-Free Conjugate Gradient
Verification of the numerical results with the FreeFem++ library – https://freefem.org/
MFCG
SIZE = 203
FreeFem++
SIZE = 203
Good agreement with FreeFemm++ library
3D Symmetric (x,y,z)
xz-plane
xy-plane
yz-plane

## Slide 14: GPU Matrix-Free Conjugate Gradient
5120 cuda cores & 12 GB memory with ~ 7TFLOPS double precision

## Slide 15: GPU Matrix-Free Conjugate Gradient
BLOCKSIZE
BLOCK ID
1
2
3
N
2
1
256
2
1
256
1
256
2
ELE_BLOCKS = numElems/BLOCKSIZE + 1
NOD_BLOCKS = numNodes/BLOCKSIZE + 1
CUDA Thread-Block Architecture:
N =
threadIdx.x
Typically optimal number of threads
GPU Grid
blockIdx.x

## Slide 16: GPU Matrix-Free Conjugate Gradient
Outline of basic steps for the GPU (CUDA) MFCG algorithm:
Ref: CUDA TOOLKIT: https://docs.nvidia.com/cuda/index.html
Get GPU device cudaGetDevice(ID)
Allocate global memory cudaMallocManaged(…)
Copy host Ke and all vectors to device cudaMemcpy(…HostToDevice)
Matrix-Free MV<<<ELE_BLOCKS,BLOCKSIZE>>>(…)
cuBLAS for linear algebra updates (ddot,daxpy,dnrm2)
UpdateVector<<<NOD_BLOCKS,BLOCKSIZE>>>(…)
Copy T device to host cudaMemcpy(…DeviceToHost)
cudaFree(…)

## Slide 17: GPU Matrix-Free Conjugate Gradient
Matrix-free matrix-vector product MFMV(dst,src,Ke)
e = blockIdx.x * BLOCKSIZE + threadIdx.x
if
(e < SIZE )
for rows in Ke[8 x 8]
extract rowindex
define tmp  0
for nodes in element
extract DOFindex
tmp[node] = tmp[node] + Ke * src
end
sum = tmp[node]
atomicAdd(&dst[DOFindex [row]], sum)
end
atomicAdd(&vec,scal)
perform n times:
vec = vec + scal
returns: vec at step n
!atomicAdd handles “races conditions” occurring in SIMD
Cuda atomicAdd operation:
SIZE: Number of Mesh Elements

## Slide 18: GPU Matrix-Free Conjugate Gradient
Timings of MFCG vs NVIDIA Amgx
Up to Size = 2503:
Memory of MFCG vs NVIDIA Amgx
Up to Size = 2503:
Ref: https://github.com/NVIDIA/AMGX
MFCG is 2.12 x times faster than the NVIDIA Amgx Solver
MFCG consumes 7.76 x times less memory than NVIDIA Amgx

## Slide 19: GPU Matrix-Free Conjugate Gradient
Maximum GPU Speed-Up = 81.81 x times for double precision

## Slide 20: GPU Matrix-Free Conjugate Gradient
Maximum mesh size = 5503 elements is computed in Wall Time = 31.31s
GPU overruns for size > 5503 (not recommended)
in-memory
out-of memory

## Slide 21: Contribution
CPU (C) implementation of MFCG method for a Large-Scale FEA of the Steady-State Heat Conduction using the Voxel-Based Technique
GPU (CUDA) implementation of MFCG method for the Acceleration and Scaling of the Large-Scale FEA up to 5503 = 166,375,000 Elements
A Performance Analysis on the Timings and Memory between:
a) the CPU MFCG method and PETSc (global matrix-assembly)
b) the GPU MFCG method and NVIDIA Amgx (global matrix-assembly)
! Both PETSc & Amgx use “Sparse-Matrix Storage” (Non-Zero Storage)

## Slide 22: Future Research
Muti-GPU (CUDA) on 4 TITAN V GPUs for Large-Scale Transient Heat-Transfer on Layer-by-Layer Process Simulation for L-PBF
MF-CG  MF-PCG (Matrix-Free Jacobi Preconditioner CG)
Hybrid MPI + Multi-GPU Scheme for High Core Scaling

## Slide 23
Questions…
Thank You

## Slide 24
High Performance Matrix-Free
Method for Large-Scale FEA
on GPUs
Petros Apostolou, Florian Dugast and Albert To*
Dept. of Mechanical Engineering and Materials Science
University of Pittsburgh
April-02-2020